Vocabulary: Advanced Mechanical Systems

- Air resistance – the force exerted by air particles on moving objects.

  - For bulky objects, air resistance is approximately proportional to the square of velocity.

  - For sleek, small objects whose shape or dimension allows air particles to stream around them, air resistance is approximately proportional to velocity.

- Efficiency – The ratio of the useful work done by a mechanical system to the energy consumed to power it.

- Impulse – a measure of the amount of force exerted on an object over time.

  - If F is the average net force exerted during a time Δt, the impulse equals .

  - The impulse visited upon an object equals the change caused in its momentum.

- Power – the rate at which energy is converted in a system.

  - For perfectly efficient systems where all energy is converted to useful work, . Since work equals force times distance and velocity is distance per time, this means power can be calculated in these situations as .

  - For electrical circuits, power is the product of current and voltage.

  - Power is measured in watts. One watt equals one joule per second.