Vocabulary: Recording Data

- Absolute error – the difference between an estimated, measured, or observed value and the true value.

  - For example, if the true value is 2.00 seconds and the estimated value is 2.15 seconds, the error is 0.15 seconds.

  - Error is a number showing how much higher or lower a value is from the actual value.

  - Error can be calculated using the following formula:

error = observed value – actual value

- Accuracy – how close a measured value of a quantity is to its actual value.

- Percent error – the difference between an estimated value and the true value, expressed as a percentage.

  - To calculate percent error, divide the error by the true value and multiply by 100.

  - For example, if the true value is 2.00 seconds and the estimated value is 2.15 seconds, the percent error is:

- Precision – how close measured values are to each other.

  - Precision describes the degree of reliability and repeatability of a measurement.

  - A set of measurements can be very precise without being very accurate.

- Resolution – a measure of the fineness with which an instrument can make a measurement.

  - For example, a stopwatch that records time to the nearest hundredth of a second has greater resolution than a stopwatch that records time to the nearest tenth of a second.

- Significant digits – digits in a measured value that were directly measured or estimated.

  - A measurement should be recorded with a number of significant digits that reflects the resolution of the instrument.